## Slide 1: WING - Wearable Interoperable Neuroprosthesis Gear
Closed Loop Battery Charger
Design Review
2024-Mar-04

## Slide 2: Closed Loop Battery Charger Coil Drive System
The CLBC system is a small enclosure that contains the coil drive circuitry and provides various user inputs and outputs. It is powered by a desktop AC adapter, which can also provide power to the ThermaZone coil cooling device.

## Slide 3: Closed Loop Battery Charger - Prototype System

## Slide 4: Closed Loop Battery Charger System - Rev A
Leverage the Wireless Link
  Wired and Wireless I/O
  User Interface
    Pushbuttons
    LEDs
    Audio
  API
Add:
  Coil Drive
    Programmable Voltage
    Programmable Frequency
    Power Monitor
  4x20 Character Display
  Real Time Clock
  uSD Memory Card
  Enclosure Temperature
  Cooler Power Output

## Slide 5: Closed Loop Battery Charger System - Rev A

## Slide 6: CLBC System Rev A - Design Approach
Leverage the Wireless Link
  nRF5340
  Open Source Development Environment – Zephyr RTOS
  CLBC is a Superset
Leverage the CLBC Prototype
  Coil Drive
  Coil Drive Power
  Display
Open Source Focus
  KiCad EDA
    Schematic Capture
    PCB Layout
    Bill of Materials
  Economical Fabrication
  Enhanced Development Tool
    Clinical
    System Developers

## Slide 7: CLBC System Rev A - Mechanicals
Use LAB2 Enclosure
  Pactec LH64-130
  6.08 x 4.26 x 1.50 inches
  Binder Coil Connector
Add
  4 x 20 Character Display
  LED(s)
  Pushbuttons
  Various Power Connectors
Removable Access Panel
  Developer I/O Connector
  Wireless Link USB Connector
  uSD Memory Card

## Slide 8: CLBC System Rev A - Mechanicals

## Slide 9: Closed Loop Battery Charger System - Rev A

## Slide 10: CLBC System Rev A - Circuit Design
Focus on Both End Users and System Developers
  Minimal End User Accessibility
  Closed System Development Accessibility
    USB Connector
    I/O Connector
  Opened System Development Accessibility
    Jumpers
    Monitor Points
Leverage Reuse
  Existing Proven Design
  Evaluation Modules

## Slide 11: CLBC System Rev A - Circuit Design

## Slide 12: CLBC Rev A Circuit Design - System Power
  Power In
    Existing Control Tower AC Power Adapter
    ThermaZone Cooler Power Output for a System Requiring a Single AC Power Adapter
    Optional Alternative Barrel Power Connector
    Battery Connector
  System Power Measurement (INA236 w/I2C Interface)
    Input Voltage
    Input Current
    Calculates Input Power
  System +3.3V
    Buck/Boost DC/DC Convertor (LTC3130-1)
    Wireless Link
    Jumper Selectable
  System +5V
    Buck/Boost DC/DC Convertor (LTC3130-1)
    Coil Drive
    Jumper Selectable Power to WL
  Multiple Voltage and Current Measurement Points
  Convenient Ground Connectors

## Slide 13: CLBC Rev A Circuit Design - Coil Drive Power
Buck/Boost DC/DC Convertor (TPS55289)
  Programmable Output Voltage
  I2C Interface
  Same as CLBC Prototype

## Slide 14: CLBC Rev A Circuit Design - Coil Drive
Same Proven Circuit used in the Control Tower, LAB2, and CLBC Prototype
Based on LT1158 - Half Bridge MOSFET Driver
System Power Measurement (INA236 w/I2C Interface)
  Coil Drive Voltage
  Coil Drive Current
  Calculates Coil Drive Power
Multiple Voltage and Current Measurement Points
Alternative Coil Drive Power Connector

## Slide 15: CLBC Rev A Circuit Design - User I_O
System Connectors
  Pushbuttons
  Display
  Recharge Coil
  Extra Pad Connected Pins for Each Connector (Future Expansion)
Audio Tone
  Duplicate of Wireless Link
Pushbuttons - 2
  Duplicate of Wireless Link
LED(s)
  Tricolor Duplicate of Wireless Link
    On Board
  Three Discrete Colors
    On Board
    Connector
Display
  OLED 4 x 20 Character
  I2C Interface
  Enhanced CLBC Prototype

## Slide 16: CLBC Rev A Circuit Design - Miscellaneous
Developer I/O Connector
  I2C
  SPI w/CS
  UART TX/RX
  Power
    +3.3V
    +5V
    VD (Power In)
    GND
  Not End User Accessible
uSD Memory Card
  Not End User Accessible
Real Time Clock
  CLBC Prototype
  I2C Interface
Thermistor
  CLBC Prototype, LAB2, CT
  I2C Interface

## Slide 17: CLBC Rev A Circuit Design - Wireless Link
Wireless Link Module Footprint
  2x8 and 2x12 Expansion Connectors
  Wireless Link USB Connector
    Not End User Accessible
  Wireless Link Power Jumper
I/O Connector SPI Select
Optional Additional Pullups
  SPI
  Pushbuttons
Audio Enable on Motherboard
Coil Drive Fault Jumper

## Slide 18: CLBC Rev A Circuit Design - Wireless Link
GPI/O Mapping
  40 Wireless Link Connections
    11 WL Specific Peripherals / Other Functions Connected to Pads and/or Jumpers
    16 CLBC Specific Functions
    6 Duplicated Functions
      LED(s)
      Pushbuttons - 2
      Audio Tone
    7 Power
  “CLBC GPIO Map 240206.xlsx”
Wireless Link Use
  “Production” Boards
  Add 2 Connectors
    2 x 8
    2 x 12
  Operate at 3.3V

## Slide 19: CLBC Rev A Circuit Design - Schematic / PCB
KiCad EDA 7.0.8
  Schematic Capture
  PCB Layout
    5.6 x 4.0 Inch
    SMT / Through Hole
    4 Layers
  3D Rendering
  Bill of Materials
    Ported to Excel
      Manufacturer Part Numbers
      Vendor Part Numbers / Links

## Slide 20: CLBC Rev A Circuit Design – PCB Real Estate

## Slide 21: CLBC Rev A Design - Status
Schematic 97% Complete
PCB Layout 97% Complete
PCB Left to Do
  Ground Plane on Back Layer
  Geographical Reannotation
  Additional Jumpers / Pads
    +5V PGOOD
    Coil Drive Fault
  Polarity Markings on Monitor Connectors
BOM 97% Complete
BOM Left to Do
  Verify a Couple of Capacitors
  Resistors
  Off Board Parts
Fabrication
  Bare PCBs
  Populate PCBs
  Mechanicals

## Slide 22: CLBC Rev A Design - Links
COSMIIC Confluence Pages
  https://cosmiic.atlassian.net/wiki/spaces/COSMIIC/pages/edit-v2/246251532
Evaluation Boards / Key Data Sheets
  TPS55289 Coil Drive Power DC/DC Convertor EVM
  INA236 Power Monitor EVM
  LTC3130-1 +3.3V/5V DC/DC Convertor EVM
  LT1158 Half Bridge Drive
  DS3231 RTC
  ADS1110 ADC
  NHD-0420CW-AB3 Display